## Slide 1: Chapter 14
JIT and Lean Operations
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Chapter 14: Learning Objectives
You should be able to:
  LO 14.1 Explain the terms lean operations and JIT
  LO 14.2 Describe the main characteristics of lean systems
  LO 14.3 List the five principles of the way lean systems function
  LO 14.4 List some of the benefits and some of the risks of lean operation
  LO 14.5 Describe the Toyota Production System (TPS)
  LO 14.6 List the three goals of a lean system and explain the importance of each
  LO 14.7 List the eight wastes according to lean philosophy
  LO 14.8 Identify and briefly discuss the four building blocks of a lean production system
  LO 14.9 Describe key lean improvement tools
  LO 14.10 Outline considerations for successful conversion from a traditional system to a lean system
  LO 14.11 Describe some of the obstacles to lean success

## Slide 3: Lean Operations
LO 14.1
Lean operation
  A flexible system of operation that uses considerably less resources than a traditional system
    Tend to achieve
      Greater productivity
      Lower costs
      Shorter cycle times
      Higher quality
Just-in-Time
  A highly coordinated processing system in which goods move through the system, and services are performed, just as they are needed

## Slide 4: Lean System Characteristics
LO 14.2
A number of characteristics are commonly found in lean systems:
  Waste reduction
  Continuous improvement
  Use of teams
  Work cells
  Visual controls
  High quality
  Minimal inventory
  Output only to match demand
  Quick changeovers
  Small lot sizes
  Lean culture

## Slide 5: Lean System Principles
LO 14.3
Five principles embody the way lean systems function:
  Identify customer values
  Focus on processes that create value
  Eliminate waste to create “flow”
  Produce only according to customer demand
  Strive for perfection

## Slide 6: Benefits & Risks of Lean Systems
LO 14.4
Key benefits
  Reduced waste
  Lower costs
  Increased quality
  Reduced cycle time
  Increased flexibility
  Increased productivity
Critical risks
  Increased stress on workers
  Fewer resources available if problems occur
  Supply chain disruptions can halt operations

## Slide 7: Lean Operations: The Beginning
LO 14.5
Lean operations began as lean manufacturing, also known as JIT, in the mid-1900s
Developed by Taiichi Ohno and Shigeo Ohno of Toyota
  Focus was on eliminating all waste from every aspect of the process
    Waste is viewed as anything that interferes with, or does not add value to, the process of producing automobiles
  Many terms used by Toyota, such as Kanban, Kaizen, and Muda, are commonly used industry wide.

## Slide 8: Lean: Ultimate Goal
LO 14.6
The ultimate goal:
  Achieve a balanced system–
    One that achieves a smooth, rapid flow of materials and/or work through the system

## Slide 9: Lean: Supporting Goals
LO 14.6
The degree to which lean’s ultimate goal is achieved depends upon how well its supporting goals are achieved:
  Eliminate disruptions
  Make the system flexible
  Eliminate waste, especially excess inventory

## Slide 10: Waste
LO 14.7
Waste
  Represents unproductive resources
  Eight sources of waste in lean systems:
    Excess inventory
    Overproduction
    Waiting time
    Unnecessary transporting
    Processing waste
    Inefficient work methods
    Product defects
    Underused people

## Slide 11: Kaizen
LO 14.7
The kaizen philosophy for attacking waste is based upon these ideas:
  Waste is the enemy, and to eliminate waste it is necessary to get the hands dirty
  Improvement should be done gradually and continuously; the goal is not big improvements done intermittently
  Everyone should be involved
  Kaizen is built on a cheap strategy, and it does not require spending great sums on technology or consultants
  It can be applied everywhere
  It is supported by a visual system
  It focuses attention where value is created
  It is process oriented
  It stresses that the main effort for improvement should come from new thinking and a new work style
  The essence of organizational learning is to learn while doing

## Slide 12: Lean: Building Blocks
LO 14.8
Product design
Process design
Personnel/organizational elements
Manufacturing planning and control

## Slide 13: Building Blocks: Product Design
LO 14.8
Four elements of product design important for lean systems:
  Standard parts
  Modular design
  Highly capable systems with quality built in
  Concurrent engineering

## Slide 14: Building Blocks: Process Design
LO 14.8
Eight aspects of process design that are important for lean systems:
  Small lot sizes
  Setup time reduction
  Manufacturing cells
  Quality improvement
  Production flexibility
  A balanced system
  Little inventory storage
  Fail-safe methods

## Slide 15: Process Design: Small Lot Sizes
LO 14.8
In the lean philosophy, the ideal lot size is one
Benefits of small lot size
  Reduced in-process inventory
    Lower carrying costs
    Less storage space is necessary
  Inspection and rework costs are less when problems with quality do occur
  Permits greater flexibility in scheduling
  Less inventory to ‘work off’ before implementing product improvements
  Increased visibility of problems
  Increased ease of balancing operations

## Slide 16: Process Design: Setup Time Reduction
LO 14.8
Small lot sizes and changing product mixes require frequent setups
Unless these are quick and relatively inexpensive, they can be prohibitive
Setup time reduction requires deliberate improvement efforts
  Single-minute exchange of die (SMED)
    A system for reducing changeover time
  Group technology may be used to reduce setup time by capitalizing on similarities in recurring operations

## Slide 17: Process Design: Manufacturing Cells
LO 14.8
One characteristic of lean production systems is multiple manufacturing cells
Benefits include
  Reduced changeover times
  High equipment utilization
  Ease of cross-training workers

## Slide 18: Process Design: Quality Improvement
LO 14.8
Quality defects during the process can disrupt the orderly flow of work
Autonomation (jidoka)
  Automatic detection of defects during production
    Two mechanisms are employed
      One for detecting defects when they occur
      Another for stopping production to correct the cause of the defects

## Slide 19: Process Design: Work Flexibility
LO 14.8
Guidelines for increasing flexibility
  Reduce downtime due to changeovers by reducing changeover time
  Use preventive maintenance on key equipment to reduce breakdowns and downtime
  Cross-train workers so they can help when bottlenecks occur or other workers are absent
  Use many small units of capacity; many small cells make it easier to shift capacity temporarily and to add or subtract capacity
  Use off-line buffers. Store infrequently used safety stock away from the production area
  Reserve capacity for important customers

## Slide 20: Process Design: Balanced System
LO 14.8
Takt time
  The cycle time needed to match customer demand for final product
  Sometimes referred to as the heartbeat of a lean system
    Takt time is often set for a work shift
    Procedure:
      Determine the net time available per shift
      If there is more than one shift per day, multiply the net time by the number of shifts
      Compute the takt time by dividing the net available time by demand

## Slide 21: Computing Takt Time - an example
LO 14.8
Given the following information, compute the takt time: Total time per shift is 480 minutes per day, and there are two shifts per day. There are two 20-minute rest breaks and a 30-minute lunch break per shift. Daily demand is 80 units.
1. Compute net time available per shift:
Total time 480 minutes
Rest breaks −40 minutes
Lunch −30 minutes
= 410 minutes per shift
2. Compute the net time available per day:
= 410 minutes per shift × 2shifts/day = 820 minutes per day
3. Compute the takt time:
Takt time = Net time available per day / Daily demand
  = 820 / 80
  = 10.25 minutes per cycle

## Slide 22: Process Design: Inventory Storage
LO 14.8
Lean systems are designed to minimize inventory storage
  Inventories are buffers that tend to cover up recurring problems that are never resolved
    Partly because they are not obvious
    Partly because the presence of inventory makes them seem less serious

## Slide 23: Process Design: Fail-Safe Methods
LO 14.8
Poka-yoke (Fail-safing)
  Building safeguards into a process to reduce or eliminate the potential for errors during a process
    Examples:
      Electric breakers
      Seatbelt fastener warnings
      ATMs that signal if a card is left in a machine
      Designing parts that can only be assembled in the correct position
      Electrical fuses and circuit breakers that interrupt electrical supply if a circuit is overloaded
      Detectors at department stores that signal if a monitoring tag hasn’t been removed from an item

## Slide 24: Building Blocks: Personnel/Organizational
LO 14.8
Five personnel/organizational elements that are important for lean systems:
  Workers as assets
  Cross-trained workers
  Continuous improvement
  Cost accounting
  Leadership/project management

## Slide 25: Personnel/Organizational: Workers as Assets
LO 14.8
Workers as assets
  Well-trained and motivated workers are the heart of the lean system
    They are given greater authority to make decisions, but more is expected of them

## Slide 26: Personnel/Organizational: Cross-Trained Workers
LO 14.8
Cross-trained workers
  Workers are trained to perform several parts of a process and operate a variety of machines
    Facilitates flexibility
    Helps in line balancing

## Slide 27: Personnel/Organizational: Continuous Improvement
LO 14.8
Continuous improvement
  Workers in lean systems have greater responsibility for quality, and they are expected to be involved in problem solving and continuous improvement
  Lean workers receive training in
    Statistical process control
    Quality improvement
    Problem solving

## Slide 28: Personnel/Organizational: Cost Accounting
LO 14.8
Cost accounting
  Activity-based costing
    Allocation of overhead to specific jobs based on their percentage of activities

## Slide 29: Personnel/Organizational: Leadership
LO 14.8
Leadership/project management
  Managers are expected to be leaders and facilitators, not order givers
  Lean systems encourage two-way communication between workers and managers

## Slide 30: Building Blocks: MPC
LO 14.8
Seven elements of manufacturing planning and control (MPC) are particularly important for lean system:
  Level loading
  Pull systems
  Visual systems
  Limited work-in-process (WIP)
  Close vendor relationships
  Reduced transaction processing
  Preventive maintenance and housekeeping

## Slide 31: MPC: Level Loading
LO 14.8
Lean systems place a strong emphasis on achieving stable, level daily mix schedules
  MPS – developed to provide level capacity loading
  Mixed model scheduling
    Three issues need to be resolved
      What is the appropriate product sequence to use?
      How many times should the sequence be repeated daily?
      How many units of each model should be produced in each cycle?

## Slide 32: MPC: Pull Systems
LO 14.8
Push system
  Work is pushed to the next station as it is completed
Pull system
  A workstation pulls output from the preceding workstation as it is needed
  Output of the final operation is pulled by customer demand or the master schedule
  Pull systems are not appropriate for all operations
    Large variations in volume, product mix, or product design will undermine the system

## Slide 33: MPC: Visual Systems
LO 14.8
Kanban
  Card or other device that communicates demand for work or materials from the preceding station
    Kanban is the Japanese word meaning “signal” or “visible record”
  Paperless production control system
  Authority to pull, or produce, comes from a downstream process
  Two main types of kanbans:
    Production kanban (p-kanban): signals the need to produce parts
    Conveyance kanban (c-kanban): signals the need to deliver parts to the next work center

## Slide 34: MPC: Limited WIP
LO 14.8
Benefits of lower WIP
  Lower carrying costs
  Increased flexibility
  Aids scheduling
  Saves costs of scrap and rework if there are design changes
  Lower cycle-time variability

## Slide 35: MPC: Close Vendor Relationships
LO 14.8
Lean systems typically have close relationships with vendors
  They are expected to provide frequent, small deliveries of high-quality goods
A key feature of many lean systems is the relatively small number of suppliers used

## Slide 36: MPC: Reduced Transaction Processing
LO 14.8
Lean systems seek to reduce costs associated with the ‘hidden factory’:
  Logistical transactions
  Balancing transactions
  Quality transactions
  Change transactions

## Slide 37: Preventive Maintenance and Housekeeping
LO 14.8
Preventive maintenance
  Maintaining equipment in good operating condition and replacing parts that have a tendency to fail before they actually do fail
Housekeeping
  Maintaining a workplace that is clean and free of unnecessary materials. It involves the following 5 behaviors to make the workplace effective
    Sort
    Straighten
    Sweep
    Standardize
    Self-discipline

## Slide 38: Lean Tools: Value Stream Mapping
LO 14.9
Value stream mapping
  A visual tool to systematically examine the flows of materials and information
    Its purpose is to help identify waste and opportunities for improvement
    Data collected:
      Times
      Distances traveled
      Mistakes
      Inefficient work methods
      Waiting times
      Information flows

## Slide 39: Lean Tools: 5W2H & Six Sigma
LO 14.9
5W2H
  A method of asking questions about a process that includes what, why, where, when, who, how, and how much
Lean and Six Sigma
  Lean and Six Sigma can be viewed as two complementary approaches to process improvement
    Lean focuses on eliminating non-value-added activity to maximize process velocity
    Six Sigma seeks to eliminate process variation
    Together the two approaches can achieve process flow and quality

## Slide 40: Transitioning to Lean Systems
LO 14.10
Make sure top management is committed and that they know what will be required
Decide which parts will need the most effort to convert
Obtain support and cooperation of workers
Begin by trying to reduce setup times while maintaining the current system
Gradually convert operations, begin at the end and work backwards
Convert suppliers to JIT
Prepare for obstacles

## Slide 41: Obstacles to Conversion
LO 14.11
Management may not be fully committed or willing to devote the necessary resources to conversion
Workers/management may not be cooperative
It can be difficult to change the organizational culture to one consistent with the lean philosophy
Suppliers may resist

## Slide 42: End of Main Content