## Slide 1: Chapter 11
Aggregate Planning and Master Scheduling
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Chapter 11: Learning Objectives
You should be able to:
  LO 11.1 Explain what aggregate planning is and how it is useful
  LO 11.2 Identify the variables decision makers have to work with in aggregate planning
  LO 11.3 Describe some of the strategies that can be used for meeting uneven demand
  LO 11.4 Describe some of the graphical and quantitative techniques planners use
  LO 11.5 Prepare aggregate plans and compute their costs
  LO 11.6 Discuss aggregate planning in services
  LO 11.7 Disaggregate an aggregate plan
  LO 11.8 Describe the master scheduling process and explain its importance

## Slide 3: Aggregate Planning
LO 11.1
Aggregate planning
  Intermediate-range capacity planning that typically covers a time horizon of 2 to up to 18 months
  Useful for organizations that experience seasonal or other variations in demand
  Goal:
    Achieve a production plan that will effectively utilize the organization’s resources to satisfy demand

## Slide 4: The Planning Sequence
LO 11.1
Access the text alternative for slide images.

## Slide 5: Why Use Aggregate Planning
LO 11.1
Why do organizations need to do aggregate planning?
  Planning
    It takes time to implement plans
  Strategic
    Aggregation is important because it is not possible to predict with accuracy the timing and volume of demand for individual items
  It is connected to the budgeting process
  It can help synchronize flow throughout the supply chain; it affects costs, equipment utilization, employment levels, and customer satisfaction

## Slide 6: Aggregation
LO 11.1
The plan must be in units of measurement that can be understood by the firm’s non-operations personnel
  Aggregate units of output per month
  Dollar value of total monthly output
  Total output by factory
  Measures that relate to capacity such as labor hours

## Slide 7: Dealing with Variation
Most organizations use rolling 3, 6, 9, and 12 month forecasts
  Forecasts are updated periodically, rather than relying on a once-a-year forecast
  This allows planners to take into account any changes in either expected demand or expected supply and to develop revised plans

## Slide 8: Dealing with Variation (cont.)
Strategies to counter variation:
  Maintain a certain amount of excess capacity to handle increases in demand
  Maintain a degree of flexibility in dealing with changes
    Hiring temporary workers
    Using overtime
  Wait as long as possible before committing to a certain level of supply capacity
    Schedule products or services with known demands first
    Wait to schedule other products until their demands become less uncertain

## Slide 9: Overview of Aggregate Planning
Access the text alternative for slide images.

## Slide 10: Demand and Supply
LO 11.2
Aggregate planners are concerned with the
  Demand quantity
    If demand exceeds capacity, attempt to achieve balance by altering capacity, demand, or both
  Timing of demand
    Even if demand and capacity are approximately equal, planners still often have to deal with uneven demand within the planning period

## Slide 11: Aggregate Planning Inputs
LO 11.2
Resources
  Workforce/production rates
  Facilities and equipment
Demand forecast
Policies
  Workforce changes
  Subcontracting
  Overtime
  Inventory levels/changes
  Back orders
Costs
  Inventory carrying
  Back orders
  Hiring/firing
  Overtime
  Inventory changes
  Subcontracting

## Slide 12: Aggregate Planning Outputs
LO 11.2
Total cost of a plan
Projected levels of
  Inventory
  Output
  Employment
  Subcontracting
  Backordering

## Slide 13: Aggregate Planning Strategies
LO 11.2
Proactive
  Alter demand to match capacity
Reactive
  Alter capacity to match demand
Mixed
  Some of each

## Slide 14: Demand Options
LO 11.2
Pricing
  Used to shift demand from peak to off-peak periods
  Price elasticity is important
Promotion
  Advertising and other forms of promotion
Back orders
  Orders are taken in one period and deliveries promised for a later period
New demand
  Create new demand to absorb excess capacity generated due to peak time demands

## Slide 15: Supply Options
LO 11.2
Hire and layoff workers
Overtime/slack time
Part-time workers
Inventories
Subcontracting

## Slide 16: Prominent Aggregate Planning Strategies
LO 11.3
Maintain a level workforce
Maintain a steady output rate
Match demand period by period
Use a combination of decision variables

## Slide 17: Aggregate Planning Pure Strategies
LO 11.3
Level capacity strategy:
  Maintaining a steady rate of regular-time output while meeting variations in demand by a combination of options:
    Inventories, overtime, part-time workers, subcontracting, and back orders
Chase demand strategy:
  Matching capacity to demand; the planned output for a period is set at the expected demand for that period

## Slide 18: Chase Approach
LO 11.3
Capacities are adjusted to match demand requirements over the planning horizon
  Advantages
    Investment in inventory is low
    Labor utilization in high
  Disadvantages
    The cost of adjusting output rates and/or workforce levels

## Slide 19: Level Approach
LO 11.3
Capacities are kept constant over the planning horizon
Advantages
  Stable output rates and workforce
Disadvantages
  Greater inventory costs
  Increased overtime and idle time
  Resource utilizations vary over time

## Slide 20: Techniques for Aggregate Planning
LO 11.4
General procedure:
  Determine demand for each period
  Determine capacities for each period
  Identify pertinent company or departmental policies
  Determine unit costs
  Develop alternative plans and costs
  Select the plan that best satisfies objectives. Otherwise return to step 5.

## Slide 21: Trial-and-Error Techniques
LO 11.4
Trial-and-error approaches consist of developing simple tables or graphs that enable planners to visually compare projected demand requirements with existing capacity
Alternatives are compared based on their total costs
Disadvantage of such an approach is that it does not necessarily result in an optimal aggregate plan

## Slide 22: Trial-and-Error Techniques (cont.)
LO 11.4
Period | 1 | 2 | 3 | 4 | 5 |  | Total
Forecast |  |  |  |  |  |  | 
Output |  |  |  |  |  |  | 
Regular time |  |  |  |  |  |  | 
Overtime |  |  |  |  |  |  | 
Subcontract |  |  |  |  |  |  | 
Output – Forecast |  |  |  |  |  |  | 
Inventory |  |  |  |  |  |  | 
Beginning |  |  |  |  |  |  | 
Ending |  |  |  |  |  |  | 
Average |  |  |  |  |  |  | 
Backlog |  |  |  |  |  |  | 
Costs |  |  |  |  |  |  | 
Output Regular |  |  |  |  |  |  | 
Overtime |  |  |  |  |  |  | 
Subcontract |  |  |  |  |  |  | 
Hire/Lay off |  |  |  |  |  |  | 
Inventory |  |  |  |  |  |  | 
Back orders |  |  |  |  |  |  | 
Total |  |  |  |  |  |  | 
TABLE 11.4 Worksheet/spreadsheet

## Slide 23: Cumulative Graph
LO 11.4
Access the text alternative for slide images.

## Slide 24: Mathematical Techniques
LO 11.4
Linear programming models
  Methods for obtaining optimal solutions to problems involving the allocation of scarce resources in terms of cost minimization or profit maximization.
Simulation models
  Computerized models that can be tested under different scenarios to identify acceptable solutions to problems

## Slide 25: Linear programming models
LO 11.5
TABLE 11.4 Worksheet/spreadsheet
 |  | Period 1 | Period 2 | Period 3 | … | Ending inventory period n | Unused capacity | Capacity
Period | Beginning inventory | 0 | h | 2h | … | (n–1)h | 0 | I0
1 | Regular time | r | r + h | r + 2h | … | r+(n–1)h | 0 | R1
 | Overtime | t | t + h | t + 2h | … | t+(n–1)h | 0 | O1
 | Subcontract | s | s + h | s + 2h | … | s+(n–1)h | 0 | S1
2 | Regular time | r + b | r | r + h | … | r+(n–2)h | 0 | R2
 | Overtime | t + b | t | t + h | … | t+(n–2)h | 0 | O2
 | Subcontract | s + b | s | s + h | … | s+(n–2)h | 0 | S2
3 | Regular time | r + 2b | r + b | r | … | r+(n–3)h | 0 | R3
 | Overtime | t + 2b | t + b | t | … | t+(n–3)h | 0 | O3
 | Subcontract | s + 2b | s + b | s | … | s+(n–3)h | 0 | S3
 | Demand |  |  |  | … |  |  | Total
r = Regular production cost per unit
f = Overtime cost per unit
s = Subcontracting cost per unit
h = Holding cost per unit period
b = Backorder cost per unit per period
n = Number of periods in planning horizon

## Slide 26: Aggregate Planning Example 1
LO 11.5
Period | 1 | 2 | 3 | 4 | 5 | 6 | Total
Forecast | 200 | 200 | 300 | 400 | 500 | 200 | 1,800
Costs
  Output
    Regular time = $2 per skateboard
    Overtime = $3 per skateboard
    Subcontract = $6 per skateboard
  Inventory = $1 per skateboard per period on average inventory
  Back orders = $5 per skateboard per period
Planners for a company that makes several models of skateboards are about to prepare an aggregate plan that will cover six periods.
They want to evaluate a plan that calls for a steady rate of regular-time output, mainly using inventory to absorb the uneven demand but allowing some backlog. Overtime and subcontracting are not used because they want steady output. They intend to start with zero inventory on hand in the first period.

## Slide 27: Aggregate Planning Example 2
LO 11.5
Period | 1 | 2 | 3 | 4 | 5 | 6 | Total
Forecast | 200 | 200 | 300 | 400 | 500 | 200 | 1,800
Output |  |  |  |  |  |  | 
Regular time | 300 | 300 | 300 | 300 | 300 | 300 | 1,800
Overtime | --- | --- | --- | --- | --- | --- | 
Subcontract | --- | --- | --- | --- | --- | --- | 
Inventory |  |  |  |  |  |  | 
Output 2 Forecast | 100 | 100 | 0 | (100) | (200) | 100 | 0
Inventory |  |  |  |  |  |  | 
Beginning | 0 | 100 | 200 | 200 | 100 | 0 | 
Ending | 100 | 200 | 200 | 100 | 0 | 0 | 
Average | 50 | 150 | 200 | 150 | 50 | 0 | 600
Backlog | 0 | 0 | 0 | 0 | 100 | 0 | 100

## Slide 28: Aggregate Planning Example 3
LO 11.5
Period | 1 | 2 | 3 | 4 | 5 | 6 | Total
Costs |  |  |  |  |  |  | 
Output |  |  |  |  |  |  | 
Regular time | $600 | $600 | $600 | $600 | $600 | $600 | $3,600
Overtime | --- | --- | --- | --- | --- | --- | 
Subcontract | --- | --- | --- | --- | --- | --- | 
Hire/Layoff | --- | --- | --- | --- | --- | --- | 
Inventory | $50 | $150 | $200 | $150 | $50 | $0 | $600
Backlog | $0 | $0 | $0 | $0 | $500 | $0 | $500
Total | $650 | $750 | $800 | $750 | $1,150 | $600 | $4,700

## Slide 29: Mathematical Techniques
Technique | Solution Approach | Characteristics
Spreadsheet | Heuristic (trial and error) | Intuitively appealing, easy to understand; solution not necessarily optimal
Linear programming | Optimizing | Computerized; linear assumptions not always valid
Simulation | Heuristic (trial and error) | Computerized model can be examined under a variety of conditions
TABLE 11.7 Summary of mathematical planning techniques

## Slide 30: Aggregate Planning in Services
LO 11.6
Hospitals:
  Aggregate planning used to allocate funds, staff, and supplies to meet the demands of patients for their medical services
Airlines:
  Aggregate planning in this environment is complex due to the number of factors involved
  Capacity decisions must take into account the percentage of seats to be allocated to various fare classes in order to maximize profit or yield
Restaurants:
  Aggregate planning in high-volume businesses is directed toward smoothing the service rate, determining workforce size, and managing demand to match a fixed capacity
  Can use inventory; however, it is perishable

## Slide 31: Aggregate Planning in Services (cont.)
LO 11.6
The resulting plan in services is a time-phased projection of service staff requirements
Aggregate planning in manufacturing and services is similar, but there are some key differences:
  Demand for service can be difficult to predict
  Capacity availability can be difficult to predict
  Labor flexibility can be an advantage in services
  Services occur when they are rendered

## Slide 32: Yield Management
LO 11.6
Yield management
  An approach to maximizing revenue by using a strategy of variable pricing; prices are set relative to capacity availability
    During periods of low demand, price discounts are offered
    During periods of peak demand, higher prices are charged
    Users of yield management include
      Airlines, restaurants, hotels, restaurants

## Slide 33: Disaggregation
LO 11.7

## Slide 34: Disaggregating the Aggregate Plan
LO 11.7
Master schedule:
  The result of disaggregating an aggregate plan
  Shows quantity and timing of specific end items for a scheduled horizon

## Slide 35: Master Scheduling
LO 11.8
The heart of production planning and control
  It determines the quantity needed to meet demand from all sources
  It interfaces with
    Marketing
    Capacity planning
    Production planning
    Distribution planning
  Provides senior management with the ability to determine whether the business plan and its strategic objectives will be achieved

## Slide 36: Time Fences
LO 11.8

## Slide 37: The Master Scheduling Process
LO 11.8
Access the text alternative for slide images.

## Slide 38: The Master Scheduling Process (cont.)
LO 11.8
The master production schedule (MPS) is one of the primary outputs of the master scheduling process
  Once a tentative MPS has been developed, it must be validated
Rough cut capacity planning (RCCP) is a tool used in the validation process
  Approximate balancing of capacity and demand to test the feasibility of a master schedule
  Involves checking the capacities of production and warehouse facilities, labor, and vendors to ensure no gross deficiencies exist that will render the MPS unworkable

## Slide 39: MPS – Forecasts and Customer Orders
LO 11.8
June July
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Forecast | 30 | 30 | 30 | 30 | 40 | 40 | 40 | 40
Beginning inventory
June July
64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Forecast | 30 | 30 | 30 | 30 | 40 | 40 | 40 | 40
Customer orders (committed) | 33 | 20 | 10 | 4 | 2 |  |  | 

## Slide 40: MPS – Projected On Hand
LO 11.8
Beginning inventory
June July
64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Forecast | 30 | 30 | 30 | 30 | 40 | 40 | 40 | 40
Customer orders (committed) | 33 | 20 | 10 | 4 | 2 |  |  | 
Projected on-hand inventory | 31 | 1 | –29 |  |  |  |  | 
Customer orders are larger than forecast in week 1; projected on-hand inventory is 64 – 33 = 31
Forecast is larger than customer orders in week 2; projected on-hand inventory is 31 – 30 = 1
Forecast is larger than customer orders in week 3; projected on-hand inventory is 1 – 30 = –29

## Slide 41: Determining MPS and Projected On Hand
LO 11.8
Week | Inventory from Previous Week | Requirements | Inventory before MPS |  | (70) MPS |  | Projected Inventory
1 | 64 | 33 | 31 |  |  |  | 31
2 | 31 | 30 | 1 |  |  |  | 1
3 | 1 | 30 | −29 | + | 70 | = | 41
4 | 41 | 30 | 11 |  |  |  | 11
5 | 11 | 40 | −29 | + | 70 | = | 41
6 | 41 | 40 | 1 |  |  |  | 1
7 | 1 | 40 | −39 | + | 70 | = | 31
8 | 31 | 40 | −9 | + | 70 | = | 61

## Slide 42: Available-to-Promise
LO 11.8
June July
64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Forecast | 30 | 30 | 30 | 30 | 40 | 40 | 40 | 40
Customer orders (committed) | 33 | 20 | 10 | 4 | 2 |  |  | 
Projected on-hand inventory | 31 | 1 | 41 | 11 | 41 | 1 | 31 | 61
MPS |  |  | 70 |  | 70 |  | 70 | 70

## Slide 43: Available-to-Promise
LO 11.8
June July
6464 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Forecast | 30 | 30 | 30 | 30 | 40 | 40 | 40 | 40
Customer orders (committed) | 33 | 20 | 10 | 4 | 2 |  |  | 
Projected on-hand inventory | 31 | 1 | 41 | 11 | 41 | 1 | 31 | 61
MPS |  |  | 70 |  | 70 |  | 70 | 70
Available-to-promise inventory (uncommitted) | 11 |  | 56 |  | 68 |  | 70 | 70

## Slide 44: End of Main Content

## Slide 45: Accessibility Content: Text Alternatives for Images

## Slide 46: The Planning Sequence - Text Alternative
Return to parent-slide containing images.
Three circles in top row: corporate strategies and policies; economic, competitive, and political conditions; aggregate demand forecasts. These all lead to the Business plan, which establishes operations and capacity strategies. This leads to the Aggregate plan, which establishes operations capacity. This leads to the Master schedule, which establishes schedules for specific products.
Return to parent-slide containing images.

## Slide 47: Overview of Aggregate Planning - Text Alternative
Return to parent-slide containing images.
First is to forecast aggregate demand for the intermediate range. Next is to develop a general plan to meet demand requirements. Lastly is to update the aggregate plan periodically (e.g., monthly).
Return to parent-slide containing images.

## Slide 48: Cumulative Graph - Text Alternative
Return to parent-slide containing images.
The x-axis is labeled with 6 periods; the y-axis with the cumulative output/demand from 0 to 2000, in increments of 400. A line and a curve are graphed. The cumulative production line begins at (0,0) and ends after the 6th period at approximately 1,800. The cumulative demand curve starts at (0,0) and has y-values slightly below the cumulative production line until the 5th period, when it crosses and jumps above the line, before equaling each other at the end of the 6th period. The spaces between the line and curve are shaded. When CP exceeds CD, a surplus output is present; when CP is less than CD, demand exceeds output.
Return to parent-slide containing images.

## Slide 49: The Master Scheduling Process - Text Alternative
Return to parent-slide containing images.
3 inputs: beginning inventory, forecast, customer orders leading to Master scheduling, which has 3 outputs: projected inventory of finished goods, master production schedule, uncommitted inventory.
Return to parent-slide containing images.