## Slide 1: Chapter 5
Strategic Capacity Planning for Products and Services
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Learning Objective: Chapter 5
You should be able to:
  LO 5.1 Name the three key questions in capacity planning
  LO 5.2 Explain the importance of capacity planning
  LO 5.3 Describe ways of defining and measuring capacity
  LO 5.4 Name several determinants of effective capacity
  LO 5.5 Discuss factors to consider when deciding whether to perform in-house or outsource
  LO 5.6 Discuss the major considerations related to developing capacity alternatives
  LO 5.7 Describe the steps used to resolve constraint issues
  LO 5.8 Briefly describe approaches that are useful for evaluating capacity alternatives

## Slide 3: Capacity Planning
LO 5.1
Capacity
  The upper limit or ceiling on the load that an operating unit can handle
  Capacity needs include
    Equipment
    Space
    Employee skills

## Slide 4: Strategic Capacity Planning
LO 5.1
Goal
  To achieve a match between the long-term supply capabilities of an organization and the predicted level of long-term demand
    Overcapacity  operating costs that are too high
    Undercapacity  strained resources and possible loss of customers

## Slide 5: Capacity Planning Questions
LO 5.1
Key questions:
  What kind of capacity is needed?
  How much is needed to match demand?
  When is it needed?
Related questions:
  How much will it cost?
  What are the potential benefits and risks?
  Are there sustainability issues?
  Should capacity be changed all at once, or through several smaller changes?
  Can the supply chain handle the necessary changes?

## Slide 6: Capacity Decisions Are Strategic
LO 5.2
Capacity decisions
  Impact the ability of the organization to meet future demands
  Affect operating costs
  Are a major determinant of initial cost
  Often involve long-term commitment of resources
  Can affect competitiveness
  Affect the ease of management
  Have become more important and complex due to globalization
  Need to be planned for in advance due to their consumption of financial and other resources

## Slide 7: Defining and Measuring Capacity
LO 5.3
Measure capacity in units that do not require updating
  Why is measuring capacity in dollars problematic?
Two useful definitions of capacity
  Design capacity
    The maximum output rate or service capacity an operation, process, or facility is designed for
  Effective capacity
    Design capacity minus allowances such as personal time and maintenance

## Slide 8: Measures of capacity
LO 5.3
Business | Inputs | Outputs
Auto manufacturing | Labor hours, machine hours | Number of cars per shift
Steel mill | Furnace size | Tons of steel per day
Oil refinery | Refinery size | Gallons of fuel per day
Farming | Number of acres, number of cows | Bushels of grain per acre per year, gallons of milk per day
Restaurant | Number of tables, seating capacity | Number of meals served per day
Theater | Number of seats | Number of tickets sold per performance
Retail sales | Square feet of floor space | Revenue generated per day
TABLE 5.1 Measures of capacity

## Slide 9: Measuring System Effectiveness
LO 5.3
Actual output
  The rate of output actually achieved
  It cannot exceed effective capacity
Efficiency
Utilization
Measured as percentages

## Slide 10: Example – Efficiency and Utilization
LO 5.3
Design Capacity = 50 trucks per day
Effective Capacity = 40 trucks per day
Actual Output = 36 trucks per day

## Slide 11: Determinants of Effective Capacity
LO 5.4
Facilities
Product and service factors
Process factors
Human factors
Policy factors
Operational factors
Supply chain factors
External factors

## Slide 12: Factors that determine effective capacity
LO 5.4
Facilities | 5. Compensation
1. Design | 6. Learning rates
2. Location | 7. Absenteeism and labor turnover
3. Layout | Policy
4. Environment | Operational
B. Product/service | Scheduling
1. Design | 2. Materials management
2. Product or service mix | 3. Quality assurance
C. Process | 4. Maintenance policies
1. Quantity capabilities | 5. Equipment breakdowns
2. Quality capabilities | G. Supply chain
D. Human factors | H. External factors
1. Job content | 1. Product standards
2. Job design | 2. Safety regulations
3. Training and experience | 3. Unions
4. Motivation | 4. Pollution control standards
TABLE 5.2 Factors that determine effective capacity

## Slide 13: Strategy Formulation
LO 5.4
Strategies are typically based on assumptions and predictions about:
  Long-term demand patterns
  Technological change
  Competitor behavior

## Slide 14: Capacity Strategies
LO 5.4
Leading
  Build capacity in anticipation of future demand increases
Following
  Build capacity when demand exceeds current capacity
Tracking
  Similar to the following strategy, but adds capacity in relatively small increments to keep pace with increasing demand

## Slide 15: Capacity Cushion
LO 5.4
Capacity cushion
  Extra capacity used to offset demand uncertainty
  Capacity cushion = 100% − utilization
  Capacity cushion strategy
    Organizations that have greater demand uncertainty typically have greater capacity cushions
    Organizations that have standard products and services generally have smaller capacity cushions

## Slide 16: Steps in Capacity Planning
LO 5.4
Estimate future capacity requirements
Evaluate existing capacity and facilities; identify gaps
Identify alternatives for meeting requirements
Conduct financial analyses
Assess key qualitative issues
Select the best alternative for the long term
Implement alternative chosen
Monitor results

## Slide 17: Forecasting Capacity Requirements
LO 5.4
Long-term considerations relate to overall level of capacity requirements
  Require forecasting demand over a time horizon and converting those needs into capacity requirements
Short-term considerations relate to probable variations in capacity requirements
  Less concerned with cycles and trends than with seasonal variations and other variations from average

## Slide 18: Calculating Processing Requirements
LO 5.4
Calculating processing requirements requires reasonably accurate demand forecasts, standard processing times, and available work time

## Slide 19: Service Capacity Planning
LO 5.4
Service capacity planning can present a number of challenges related to:
  The need to be near customers
    Convenience
  The inability to store services
    Cannot store services for consumption later
  The degree of demand volatility
    Volume and timing of demand
    Time required to service individual customers

## Slide 20: Demand Management Strategies
LO 5.4
Strategies used to offset capacity limitations and that are intended to achieve a closer match between supply and demand
  Pricing
  Promotions
  Discounts
  Other tactics to shift demand from peak periods into slow periods

## Slide 21: In-House or Outsource?
LO 5.5
Once capacity requirements are determined, the organization must decide whether to produce a good or service itself or outsource
Factors to consider:
  Available capacity
  Expertise
  Quality considerations
  The nature of demand
  Cost
  Risks

## Slide 22: Developing Capacity Alternatives
LO 5.6
Things that can be done to enhance capacity management:
  Design flexibility into systems
  Take stage of life cycle into account
  Take a “big-picture” approach to capacity changes
  Prepare to deal with capacity “chunks”
  Attempt to smooth capacity requirements
  Identify the optimal operating level
  Choose a strategy if expansion is involved

## Slide 23: Bottleneck Operation
LO 5.6
An operation in a sequence of operations whose capacity is lower than that of the other operations

## Slide 24: Optimal Operating Level
LO 5.6

## Slide 25: Economies and Diseconomies of Scale
LO 5.6
Economies of scale
  If output rate is less than the optimal level, increasing the output rate results in decreasing average per unit costs
Diseconomies of scale
  If the output rate is more than the optimal level, increasing the output rate results in increasing average costs per unit

## Slide 26: Economies of Scale
LO 5.6
Economies of scale
  If output rate is less than the optimal level, increasing the output rate results in decreasing average per unit costs
  Reasons for economies of scale:
    Fixed costs are spread over a larger number of units
    Construction costs increase at a decreasing rate as facility size increases
    Processing costs decrease due to standardization

## Slide 27: Diseconomies of Scale
LO 5.6
Diseconomies of scale
  If the output rate is more than the optimal level, increasing the output rate results in increasing average per unit costs
  Reasons for diseconomies of scale
    Distribution costs increase due to traffic congestion and shipping from a centralized facility rather than multiple smaller facilities
    Complexity increases costs
    Inflexibility can be an issue
    Additional levels of bureaucracy

## Slide 28: Facility Size and Optimal Operating Level
LO 5.6

## Slide 29: Constraint Management
LO 5.7
Constraint
  Something that limits the performance of a process or system in achieving its goals
  Categories
    Market
    Resource
    Material
    Financial
    Knowledge or competency
    Policy

## Slide 30: Resolving Constraint Issues
LO 5.7
Identify the most pressing constraint
Change the operation to achieve maximum benefit, given the constraint
Make sure other portions of the process are supportive of the constraint
Explore and evaluate ways to overcome the constraint
Repeat the process until the constraint levels are at acceptable levels

## Slide 31: Evaluating Alternatives
LO 5.8
Alternatives should be evaluated from varying perspectives
  Economic
    Is it economically feasible?
    How much will it cost?
    How soon can we have it?
    What will operating and maintenance costs be?
    What will its useful life be?
    Will it be compatible with present personnel and present operations?
  Non-economic
    Public opinion

## Slide 32: Evaluating Alternatives (cont.)
LO 5.8
Techniques for Evaluating Alternatives
  Cost-volume analysis
  Financial analysis
  Decision theory
  Waiting-line analysis
  Simulation

## Slide 33: Cost-Volume Analysis
LO 5.8
Cost-volume analysis
  Focuses on the relationship between cost, revenue, and volume of output
    Fixed Costs (FC)
      Tend to remain constant regardless of output volume
    Variable Costs (VC)
      Vary directly with volume of output
      VC = Quantity(Q) × variable cost per unit (v)
    Total Cost
      TC = FC + VC
    Total Revenue (TR)
      TR = revenue per unit (R) × Q

## Slide 34: Break-Even Point (BEP)
LO 5.8
BEP
  The volume of output at which total cost and total revenue are equal
  Profit (P) = TR – TC = R × Q – (FC + v × Q)
        = Q(R – v) – FC

## Slide 35: Cost-Volume Relationships
LO 5.8
Access the text alternative for slide images.

## Slide 36: Cost-Volume Relationships (cont.)
LO 5.8
Capacity alternatives may involve step costs, which are costs that increase stepwise as potential volume increases
  The implication of such a situation is the possible occurrence of multiple break-even quantities
Access the text alternative for slide images.

## Slide 37: Cost-Volume Analysis Assumptions
LO 5.8
Cost-volume analysis is a viable tool for comparing capacity alternatives if certain assumptions are satisfied
  One product is involved
  Everything produced can be sold
  The variable cost per unit is the same regardless of volume
  Fixed costs do not change with volume changes, or they are step changes
  The revenue per unit is the same regardless of volume
  Revenue per unit exceeds variable cost per unit

## Slide 38: Financial Analysis
LO 5.8
Cash flow
  The difference between cash received from sales and other sources and cash outflow for labor, material, overhead, and taxes
Present value
  The sum, in current value, of all future cash flow of an investment proposal

## Slide 39: Operations Strategy
LO 5.8
Capacity planning impacts all areas of the organization
  It determines the conditions under which operations will have to function
  Flexibility allows an organization to be agile
    It reduces the organization’s dependence on forecast accuracy and reliability
    Many organizations utilize capacity cushions to achieve flexibility
  Bottleneck management is one way by which organizations can enhance their effective capacities
  Capacity expansion strategies are important organizational considerations
    Expand-early strategy
    Wait-and-see strategy
  Capacity contraction is sometimes necessary
    Capacity disposal strategies become important under these
    conditions

## Slide 40: End of Main Content

## Slide 41: Accessibility Content: Text Alternatives for Images

## Slide 42: Cost-Volume Relationships - Text Alternative
Return to parent-slide containing images.
The first graph has a horizontal line for Fixed Cost, a positive slope line for Total variable cost, and a parallel line labeled Total Cost = VC + FC. The second graph has a line resembling y=x labeled Total Revenue. The third graph has the Total Revenue line, with a lower-sloped line intersecting. The point where the lines cross is the BEP units. Above that line and below the TR line is profit; below that line and above the TR line is loss. The fourth graph shows a positive-slope line, where the part of the line above the x-axis is labeled profit, and below is labeled Loss. The fifth graph shows two intersecting lines labeled Profit from alternative A and Profit from alternative B. They intersect at the point of indifference.
Return to parent-slide containing images.

## Slide 43: Cost-Volume Relationships (cont.) - Text Alternative
Return to parent-slide containing images.
Part A is titled Step fixed costs and variable costs. The steps are made up of triangles with fixed cost horizontal and FC+VC=TC making up the step. This pattern repeats for 1, 2, and 3 machines. Part B is titled Multiple break-even points, and also has three steps, but only areas 2 and 3 have BEPs.
Return to parent-slide containing images.