## Slide 1: Chapter 10
Quality Control
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Chapter 10: Learning Objectives
You should be able to:
  LO 10.1 Explain the need for quality control
  LO 10.2 Discuss the basic issues of inspection
  LO 10.3 List and briefly explain the elements of the control process
  LO 10.4 Explain how control charts are used to monitor a process, and the concepts that underlie their use
  LO 10.5 Use and interpret control charts
  LO 10.6 Perform run tests to check for nonrandomness in process output
  LO 10.7 Assess process capability

## Slide 3: What Is Quality Control?
LO 10.1
Quality control
  A process that evaluates output relative to a standard and takes corrective action when output doesn’t meet standards
    If results are acceptable no further action is required
    Unacceptable results call for correction action
  Inspection alone is not sufficient to achieve a reasonable level of quality
    Most organizations rely upon some inspection and a great deal of process control to achieve an acceptable level of quality

## Slide 4: Phases of Quality Assurance
LO 10.1

## Slide 5: Inspection
LO 10.2
Inspection
  An appraisal activity that compares goods or services to a standard
  Inspection issues:
    How much to inspect and how often
    At what points in the process to inspect
    Whether to inspect in a centralized or on-site location
    Whether to inspect attributes or variables

## Slide 6: How Much to Inspect
LO 10.2
Access the text alternative for slide images.

## Slide 7: Where to Inspect in the Process
LO 10.2
Typical inspection points:
  Raw materials and purchased parts
  Finished products
  Before a costly operation
  Before an irreversible process
  Before a covering process

## Slide 8: Example of inspection at a Hotel/Motel
LO 10.2
Inspection Point | Characteristics
Accounting/billing | Accuracy, timeliness
Building and grounds | Appearance and safety
Main desk | Appearance, waiting times, accuracy of bills
Maid service | Completeness, productivity
Personnel | Appearance, manners, productivity
Reservations/occupancy | Over/underbooking, percent occupancy
Restaurants | Kitchen, menus, meals, bills
Room service | Waiting time, quality of food
Supplies | Ordering, receiving, inventories

## Slide 9: Off-Site vs. On-Site Inspection
LO 10.2
Effects on cost and level of disruption are a major issue in selecting centralized versus on-site inspection
  Off-Site
    Specialized tests that may best be completed in a lab
      More specialized testing equipment
      More favorable testing environment
  On-Site
    Quicker decisions are rendered
    Avoid introduction of extraneous factors
    Quality at the source

## Slide 10: Statistical Process Control (SPC)
LO 10.2
Quality control seeks quality of conformance
    A product or service conforms to specifications
A tool used to help in this process:
  SPC
    Statistical evaluation of the output of a process
    Helps us to decide if a process is “in control” or if corrective action is needed

## Slide 11: Process Variability
LO 10.2
Two basic questions concerning variability:
  Issue of process control
    Are the variations random? If nonrandom variation is present, the process is said to be unstable.
  Issue of process capability
    Given a stable process, is the inherent variability of the process within a range that conforms to performance criteria?

## Slide 12: Variation
LO 10.2
Variation
  Random (common cause) variation:
    Natural variation in the output of a process, created by countless minor factors
  Assignable (special cause) variation:
    A variation whose cause can be identified
    A nonrandom variation

## Slide 13: Sampling and Sampling Distribution
LO 10.2
SPC involves periodically taking samples of process output and computing sample statistics:
  Sample means
  The number of occurrences of some outcome
Sample statistics are used to judge the randomness of process variation

## Slide 14: Sampling and Sampling Distribution (cont.)
LO 10.3
FIGURE 10.4A The sampling distribution of means is normal, and it has less variability than the process distribution, which might not be normal

## Slide 15: Control Process
LO 10.3
Sampling and corrective action are only a part of the control process
Steps required for effective control:
  Define: What is to be controlled?
  Measure: How will measurement be accomplished?
  Compare: There must be a standard of comparison
  Evaluate: Establish a definition of out of control
  Correct: Uncover the cause of nonrandom variability and fix it
  Monitor: Verify that the problem has been eliminated

## Slide 16: Control Charts: The Voice of the Process
LO 10.4
Control chart
  A time-ordered plot of representative sample statistics obtained from an ongoing process (for example, sample means), used to distinguish between random and nonrandom variability
  Control limits
    The dividing lines between random and nonrandom deviations from the mean of the distribution
    Upper and lower control limits define the range of acceptable variation

## Slide 17: Control Chart
LO 10.4
Each point on the control chart represents a sample of n observations
Access the text alternative for slide images.

## Slide 18: Errors
LO 10.4
Type I error
  Concluding a process is not in control when it actually is.
    The probability of rejecting the null hypothesis when the null hypothesis is true
    Manufacturer’s risk
Type II error
  Concluding a process is in control when it is not.
    The probability of failing to reject the null hypothesis when the null hypothesis is false
    Consumer’s risk

## Slide 19: Type I Error
LO 10.4

## Slide 20: Observations from Sample Distribution
LO 10.4

## Slide 21: Control Charts for Variables
LO 10.5
Variables generate data that are measured
  Mean control charts
    Used to monitor the central tendency of a process
      “x-bar” charts
  Range control charts
    Used to monitor the process dispersion
      R charts

## Slide 22: Establishing Control Limits
LO 10.5

## Slide 23: X-Bar Chart: Control Limits
LO 10.5
Used to monitor the central tendency of a process

## Slide 24: Range Chart: Control Limits
LO 10.5
Used to monitor process dispersion

## Slide 25: Factors for Three Sigma Control Charts
LO 10.5
 |  |  | FACTORS FOR R CHARTS
Number of Observations in Sample, n | Factor for Chart, A2 | Lower Control Limit, D3 | Upper Control Limit, D4
2 | 1.88 | 0 | 3.27
3 | 1.02 | 0 | 2.57
4 | 0.73 | 0 | 2.28
5 | 0.58 | 0 | 2.11
6 | 0.48 | 0 | 2.00
7 | 0.42 | 0.08 | 1.92
8 | 0.37 | 0.14 | 1.86
9 | 0.34 | 0.18 | 1.82
10 | 0.31 | 0.22 | 1.78
11 | 0.29 | 0.26 | 1.74
12 | 0.27 | 0.28 | 1.72
13 | 0.25 | 0.31 | 1.69
14 | 0.24 | 0.33 | 1.67
15 | 0.22 | 0.35 | 1.65
16 | 0.21 | 0.36 | 1.64
17 | 0.20 | 0.38 | 1.62
18 | 0.19 | 0.39 | 1.61
19 | 0.19 | 0.40 | 1.60
20 | 0.18 | 0.41 | 1.59
TABLE 10.3
Factors for three-sigma control limits for X and R charts
Source: Adapted from Eugene Grant and Richard Leavenworth, Statistical Quality Control, 5th ed. Copyright ©1980 McGraw-Hill Companies, Inc. Used with permission

## Slide 26: Mean and Range Charts A
LO 10.5
Access the text alternative for slide images.

## Slide 27: Mean and Range Charts B
LO 10.5

## Slide 28: Using Mean and Range Charts
LO 10.5
To determine initial control limits:
  Obtain 20 to 25 samples
  Compute appropriate sample statistics
  Establish preliminary control limits
  Determine if any points fall outside of the control limits
    If you find no out-of-control signals, assume the process is in control
    If you find an out-of-control signal, search for and correct the assignable cause of variation
  Resume the process and collect another set of observations on which to base control limits
  Plot the data on the control chart and check for out-of-control signals

## Slide 29: Control Charts for Attributes
LO 10.5
Attributes generate data that are counted.
  p-chart
    Control chart used to monitor the proportion of defectives in a process
  c-chart
    Control chart used to monitor the number of defects per unit

## Slide 30: Use a p-chart:
LO 10.5
When observations can be placed into two categories
  Good or bad
  Pass or fail
  Operate or don’t operate
When the data consists of multiple samples of several observations each

## Slide 31: p-chart Control Limits
LO 10.5

## Slide 32: Use a c-chart:
LO 10.5
Use only when the number of occurrences per unit of measure can be counted; non-occurrences cannot be counted.
  Scratches, chips, dents, or errors per item
  Cracks or faults per unit of distance
  Breaks or tears per unit of area
  Bacteria or pollutants per unit of volume
  Calls, complaints, failures per unit of time

## Slide 33: Managerial Considerations
LO 10.5
At what points in the process to use control charts
What size samples to take
Sample frequency
What type of control chart to use
  Variables
  Attributes

## Slide 34: Run Tests
LO 10.6
Even if a process appears to be in control, the data may still not reflect a random process
Analysts often supplement control charts with a run test
  Run test
    A test for patterns in a sequence
  Run
    Sequence of observations with a certain characteristic

## Slide 35: Nonrandom Patterns
LO 10.6
Access the text alternative for slide images.

## Slide 36: Process Capability
LO 10.7
Once a process has been determined to be stable, it is necessary to determine if the process is capable of producing output that is within an acceptable range
  Tolerances or specifications
    Range of acceptable values established by engineering design or customer requirements
  Process variability
    Natural or inherent variability in a process
  Process capability
    The inherent variability of process output (process width) relative to the variation allowed by the design specification (specification width)

## Slide 37: Process Capability (cont.)
LO 10.7
Access the text alternative for slide images.

## Slide 38: Cp
LO 10.7

## Slide 39: Cpk
LO 10.7
Used when a process is not centered at its target, or nominal, value

## Slide 40: Improving Process Capability
LO 10.7
Simplify
Standardize
Mistake-proof
Upgrade equipment
Automate

## Slide 41: Taguchi Loss Function
LO 10.7

## Slide 42: Limitations of Capability Measures
LO 10.7
There are several risks of using capability measures:
  The process may not be stable
  The process output may not be normally distributed
  The process is not centered but Cp is used

## Slide 43: Operations Strategy
Quality is a primary consideration for nearly all customers
  Achieving and maintaining quality standards is of strategic importance to all business organizations
    Product and service design
    Increase capability in order to move from extensive use of control charts and inspection to achieve desired quality outcomes

## Slide 44: End of Main Content

## Slide 45: Accessibility Content: Text Alternatives for Images

## Slide 46: How Much to Inspect - Text Alternative
Return to parent-slide containing images.
Three curves graphed: "cost of passing defectives" starts high then curves low; "cost of inspection" is a line starting at (0,0) that increases; the "total cost" curve is the addition of the two previous. The point on "total cost" above the intersection of the first two curves is labeled "Optimal."
Return to parent-slide containing images.

## Slide 47: Control Chart - Text Alternative
Return to parent-slide containing images.
Between the upper and lower control lines is the center dotted line, which represents the mean of the distribution. The data points fall between the two control lines 99.7% of the time, and are normal variation due to chance. Points that fall outside either control line are abnormal variation due to assignable sources.
Return to parent-slide containing images.

## Slide 48: Mean and Range Charts A - Text Alternative
Return to parent-slide containing images.
In part A, the sampling distribution for each point increases as the mean increases, while the range chart does not reveal the shift. In part B, the variability becomes larger for each sample point, but the mean chart does not reveal the shift. The range charge does reveal the increase in variability.
Return to parent-slide containing images.

## Slide 49: Nonrandom Patterns - Text Alternative
Return to parent-slide containing images.
A trend occurs when there is a sustained upward or downward movement. In this example, the points are generally increasing, with occasional dips. Cycles occur when there is a wave pattern. In this example, the graph starts high, then dips low, then high again, and so on. Bias occurs when there are too many observations on one side of the center line. In this example, almost all of the points are below the center line. Too much dispersion occurs when the values are too spread out. In this example, points jump up and down, but not in any pattern.
Return to parent-slide containing images.

## Slide 50: Process Capability (cont.) - Text Alternative
Return to parent-slide containing images.
The first curve has its lower and upper specification at the ends of the distribution - process variability seems to just match specifications. The second curve has its lower and upper specification beyond the ends of the distribution - process variability is well within specifications. The third curve has its lower and upper specification inside the ends of the distribution - process variability exceeds specifications.
Return to parent-slide containing images.