## Slide 1: Chapter 16
Scheduling
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Chapter 16: Learning Objectives
You should be able to:
  LO 16.1 Explain what scheduling involves and the importance of good scheduling
  LO 16.2 Compare product and service scheduling hierarchies
  LO 16.3 Describe scheduling needs in high-volume systems
  LO 16.4 Describe scheduling needs in intermediate-volume systems
  LO 16.5 Describe scheduling needs in job shops
  LO 16.6 Use and interpret Gantt charts
  LO 16.7 Use the assignment method for loading
  LO 16.8 Give examples of commonly used priority rules
  LO 16.9 Discuss the theory of constraints and that approach to scheduling
  LO 16.10 Summarize some of the unique problems encountered in service systems, and describe some of the approaches used for scheduling service systems

## Slide 3: Scheduling
LO 16.1
Scheduling:
  Establishing the timing of the use of equipment, facilities and human activities in an organization
Effective scheduling can yield
    Cost savings
    Increases in productivity
    Other benefits

## Slide 4: Scheduling Context
LO 16.1
Scheduling is constrained by multiple system design and operations decisions
  System capacity
  Product and/or service design
  Equipment selection
  Worker selection and training
  Aggregate planning and master scheduling

## Slide 5: Scheduling Hierarchies
LO 16.2
Access the text alternative for slide images.

## Slide 6: High Volume Systems
LO 16.3
Flow system
  High-volume system in which all jobs follow the same sequence
  Flow system scheduling
    The goal is to achieve a smooth rate of flow of goods or customers through the system in order to get high utilization of labor and equipment

## Slide 7: High-Volume: Scheduling Difficulties
LO 16.3
Few flow systems are entirely dedicated to a single product or service
  Each product change requires
    Slightly different inputs of parts
    Slightly different materials
    Slightly different processing requirements that must be scheduled into the line
  Need to avoid excessive inventory buildup
  Disruptions may result in less-than-desired output

## Slide 8: High-Volume Success Factors
LO 16.3
The following factors often dictate the success of high-volume systems:
  Process and product design
  Preventive maintenance
  Rapid repair when breakdowns occur
  Optimal product mixes
  Minimization of quality problems
  Reliability and timing of supplies

## Slide 9: Intermediate-Volume Systems 1
LO 16.4
Outputs fall between the standardized type of output of high-volume systems and the make-to-order output of job shops
Output rates are insufficient to warrant continuous production
  Rather, it is more economical to produce intermittently
    Work centers periodically shift from one product to another

## Slide 10: Intermediate-Volume Systems 2
LO 16.4
Three basic issues:
  Run size of jobs
  The timing of jobs
  The sequence in which jobs will be produced

## Slide 11: Intermediate-Volume Systems 3
LO 16.4
Important considerations
  Setup cost
  Usage is not always as smooth as assumed in the economic lot size model
Alternative scheduling approach
  Base production on a master schedule developed from customer orders and forecasted demand

## Slide 12: Low-Volume Systems
LO 16.5
Job shop scheduling
  Scheduling for low-volume systems with many variations in requirements
    Make-to-order products
    Processing requirements
    Material requirements
    Processing time
    Processing sequence and setups
  A complex scheduling environment
    It is impossible to establish firm schedules until actual job orders are received

## Slide 13: Low-Volume Systems: Loading
LO 16.5
Loading
  The assignment of jobs to processing centers
  Gantt chart
    Used as a visual aid for loading and scheduling purposes
    Purpose of the Gantt chart is to organize and visually display the actual or intended use of resources in a time framework
    Managers may use the charts for trial-and-error schedule development to get an idea of what different arrangements would involve

## Slide 14: Gantt Charts
LO 16.6
Load chart
  A Gantt chart that shows the loading and idle times for a group of machines or list of departments

## Slide 15: Loading Approaches
LO 16.6
Infinite loading
  Jobs are assigned to workstations without regard to the capacity of the work center
Finite loading
  Jobs are assigned to work centers taking into account the work center capacity and job processing times

## Slide 16: Scheduling Approaches
LO 16.6
Forward scheduling
  Scheduling ahead from some point in time
  Used when the question is:
    “How long will it take to complete this job?”
Backward scheduling
  Scheduling backwards from some due date
  Used when the question is:
    “When is the latest this job can be started and still be completed on time?”

## Slide 17: Input/Output Control
LO 16.6
Monitors the work flow and queue lengths at work centers. These controls help in
avoiding overloading a work center
keeping the queue within manageable limits
matching the work center capacity with the incoming work

## Slide 18: Gantt Charts (cont.)
LO 16.6
Schedule chart
  A Gantt chart that shows the orders or jobs in progress and whether they are on schedule

## Slide 19: Assignment
LO 16.7
Assignment model
  A linear programming model for optimal assignment of tasks and resources
Hungarian method
  Method of assigning jobs by a one-for-one matching to identify the lowest cost solution

## Slide 20: Hungarian Method
LO 16.7
Row reduction: subtract the smallest number in each row from every number in the row
  Enter the result in a new table
Column reduction: subtract the smallest number in each column from every number in the column
  Enter the result in a new table
Test whether an optimum assignment can be made
  Determine the minimum number of lines needed to cross out all zeros
  If the number of lines equals the number of rows, an optimum assignment is possible. Go to step 6.
  If not, go to step 4

## Slide 21: Hungarian Method (cont.)
LO 16.7
If the number of lines is less than the number of rows, modify the table:
  Subtract the smallest number from every uncovered number in the table
  Add the smallest uncovered number to the numbers at intersections of cross-out lines
  Numbers crossed out but not at intersections of cross-out lines carry over unchanged to the next table
Repeat steps 3 and 4 until an optimal table is obtained
Make the assignments
  Begin with rows or columns with only one zero
  Match items that have zeros, using only one match for each row and each column
  Eliminate both the row and the column after the match

## Slide 22: Example: Hungarian Method 1
LO 16.7
Determine the optimum assignment of jobs to workers for the following data:
Worker
 |  | A | B | C | D
 | 1 | 8 | 6 | 2 | 4
Job | 2 | 6 | 7 | 11 | 10
 | 3 | 3 | 5 | 7 | 6
 | 4 | 5 | 10 | 12 | 9

## Slide 23: Example: Hungarian Method 2
LO 16.7
Worker
 |  | A | B | C | D | Row minimum
 | 1 | 8 | 6 | 2 | 4 | 2
Job | 2 | 6 | 7 | 11 | 10 | 6
 | 3 | 3 | 5 | 7 | 6 | 3
 | 4 | 5 | 10 | 12 | 9 | 5
Subtract the smallest number in each row from every number in the row
Worker
 |  | A | B | C | D
 | 1 | 6 | 4 | 0 | 2
Job | 2 | 0 | 1 | 5 | 4
 | 3 | 0 | 2 | 4 | 3
 | 4 | 0 | 5 | 7 | 4

## Slide 24: Example: Hungarian Method 3
LO 16.7
Worker
 |  | A | B | C | D
 | 1 | 6 | 4 | 0 | 2
Job | 2 | 0 | 1 | 5 | 4
 | 3 | 0 | 2 | 4 | 3
 | 4 | 0 | 5 | 7 | 4
Column min. |  | 0 | 1 | 0 | 2
Subtract the smallest number in each column from every number in the column
Worker
 |  | A | B | C | D
 | 1 | 6 | 3 | 0 | 0
Job | 2 | 0 | 0 | 5 | 2
 | 3 | 0 | 1 | 4 | 1
 | 4 | 0 | 4 | 7 | 2

## Slide 25: Example: Hungarian Method 4
LO 16.7
Worker
 |  | A | B | C | D
 | 1 | 6 | 3 | 0 | 0
Job | 2 | 0 | 0 | 5 | 2
 | 3 | 0 | 1 | 4 | 1
 | 4 | 0 | 4 | 7 | 2
Determine the minimum number of lines needed to cross out all zeros. (Try to cross out as many zeros as possible when drawing lines.)
Since only three lines are needed to cross out all zeros and the table has four rows, this is not the optimum. Note: The smallest uncovered value is 1.

## Slide 26: Example: Hungarian Method 5
LO 16.7
Worker
 |  | A | B | C | D
 | 1 | 6 | 3 | 0 | 0
Job | 2 | 0 | 0 | 5 | 2
 | 3 | 0 | 1 | 4 | 1
 | 4 | 0 | 4 | 7 | 2
Subtract the smallest uncovered value from every uncovered number, and add it to the values at the intersection of covering lines
Worker
 |  | A | B | C | D
 | 1 | 7 | 3 | 0 | 0
Job | 2 | 1 | 0 | 5 | 2
 | 3 | 0 | 0 | 3 | 0
 | 4 | 0 | 3 | 6 | 1

## Slide 27: Example: Hungarian Method 6
LO 16.7
Worker
 |  | A | B | C | D
 | 1 | 7 | 3 | 0 | 0
Job | 2 | 1 | 0 | 5 | 2
 | 3 | 0 | 0 | 3 | 0
 | 4 | 0 | 3 | 6 | 1
Determine the minimum number of lines needed to cross out all zeros. (Try to cross out as many zeros as possible when drawing lines.)
Since four lines are needed to cross out all zeros and the table has four rows, this an optimal assignment can be made

## Slide 28: Example: Hungarian Method 7
LO 16.7
Worker
 |  | A | B | C | D
 | 1 | 7 | 3 | 0 | 0
Job | 2 | 1 | 0 | 5 | 2
 | 3 | 0 | 0 | 3 | 0
 | 4 | 0 | 3 | 6 | 1
Make assignments: Start with rows and columns with only one zero. Match jobs with workers that have a zero.
Assignment | Cost
2-B | $7
4-A | $5
1-C | $2
3-D | $6
Total | $20

## Slide 29: Sequencing
LO 16.8
Sequencing
  Determine the order in which jobs at a work center will be processed
Priority rules
  Simple heuristics used to select the order in which jobs will be processed
  The rules generally assume that job setup cost and time are independent of processing sequence
    Job time
      Time needed for setup and processing of a job

## Slide 30: Priority Rules
LO 16.8
FCFS - first come, first served
SPT - shortest processing time
EDD - earliest due date
CR - critical ratio
S/O - slack per operation
Rush - emergency

## Slide 31: Priority Rules: Assumptions
LO 16.8
The set of jobs is known; no new orders arrive after processing begins and no jobs are canceled
Setup time is independent of processing sequence
Setup time is deterministic
Processing times are deterministic
There will be no interruptions in processing such as machine breakdowns or accidents

## Slide 32: Sequence: Performance Metrics
LO 16.8
Common performance metrics:
  Job flow time
    This is the amount of time it takes from when a job arrives until it is complete
    It includes not only processing time but also any time waiting to be processed
  Job lateness
    This is the amount of time the job completion time is expected to exceed the date the job was due or promised to a customer
  Makespan
    The total time needed to complete a group of jobs from the beginning of the first job to the completion of the last job
  Average number of jobs
    Jobs that are in a shop are considered to be WIP inventory

## Slide 33: Two Work Center Sequencing
LO 16.8
Johnson’s Rule
  Technique for minimizing makespan for a group of jobs to be processed on two machines or at two work centers
    Minimizes total idle time
    Several conditions must be satisfied

## Slide 34: Johnson’s Rule Conditions
LO 16.8
Job time must be known and constant for each job at the work center
Job times must be independent of sequence
Jobs must follow same two-step sequence
All jobs must be completed at the first work center before moving to second work center

## Slide 35: Johnson’s Rule: Optimum Sequence
LO 16.8
List the jobs and their times at each work center
Select the job with the shortest time
  If the shortest time is at the first work center, schedule that job first
  If the shortest time is at the second work center, schedule the job last
  Break ties arbitrarily
Eliminate the job from further consideration
Repeat steps 2 and 3, working toward the center of the sequence, until all jobs have been scheduled

## Slide 36: Minimizing Scheduling Difficulties
LO 16.8
Many steps can be taken to minimize scheduling-related problems, such as:
Set realistic due dates
Focus on bottleneck operations
Consider splitting lots for larger jobs

## Slide 37: Theory of Constraints 1
LO 16.9
Theory of constraints
  Production planning approach that emphasizes balancing flow throughout a system, and pursues a perpetual five-step improvement process centered around the system’s currently most restrictive constraint
    Bottleneck operations limit system output
      Therefore, schedule bottleneck operations in a way that minimizes their idle times
    Drum-buffer-rope
      Drum = the schedule
      Buffer = potentially constraining resources outside of the bottleneck
      Rope = represents synchronizing the sequence of operations to ensure effective use of the bottleneck operations

## Slide 38: Theory of Constraints 2
LO 16.9
Varying batch sizes to achieve greatest output of bottleneck operations
  Process batch
    The economical quantity to produce upon the activation of a given operation
  Transfer batch
    The quantity to be transported from one operation to another, assumed to be smaller than the first operation’s process batch

## Slide 39: Theory of Constraints 3
LO 16.9
Improving bottleneck operations:
  Determine what is constraining the operation
  Exploit the constraint (i.e., make sure the constraining resource is used to its maximum)
  Subordinate everything to the constraint (i.e., focus on the constraint)
  Determine how to overcome (eliminate) the constraint
  Repeat the process for the next highest constraint

## Slide 40: Theory of Constraints: Metrics
LO 16.9
Three important theory of constraints metrics:
  Throughput
    The rate at which the system generates money through sales
  Inventory
    Inventory represents money tied up in goods and materials used in a process
  Operating expense
    All the money the system spends to convert inventory into throughput: this includes utilities, scrap, depreciation, and so on

## Slide 41: Service Operation Problems
LO 16.10
Service scheduling often presents challenges not found in manufacturing
  These are primarily related to:
    The inability to store or inventory services
    The random nature of service requests
Service scheduling may involve scheduling:
  Customers
  Workforce
  Equipment

## Slide 42: Scheduling Service Operations
LO 16.10
Scheduling customers: demand management
  Appointment systems
    Controls customer arrivals for service
  Reservation systems
    Enable service systems to formulate a fairly accurate estimate demand on the system for a given time period
Scheduling the workforce: capacity management
  Cyclical scheduling
    Employees are assigned to work shifts or time slots, and have days off, on a repeating basis

## Slide 43: End of Main Content

## Slide 44: Accessibility Content: Text Alternatives for Images

## Slide 45: Scheduling Hierarchies - Text Alternative
Return to parent-slide containing images.
Manufacturing: Aggregate Planning down to Master Production Schedule, down to Material Requirements Planning, down to Shop Floor Schedule; Service: Aggregate Planning down to Master Schedule, down to Monthly or Weekly Schedule, down to Daily Schedule.
Return to parent-slide containing images.