## Slide 1: Chapter 13
MRP and ERP
Operations Management
FOURTEENTH EDITION
William J. Stevenson

## Slide 2: Chapter 13: Learning Objectives
You should be able to:
  LO 13.1 Describe the conditions under which MRP is most appropriate
  LO 13.2 Describe the inputs, outputs, and nature of MRP processing
  LO 13.3 Explain how requirements in a master production schedule are translated into material requirements for lower-level items
  LO 13.4 Discuss the benefits and requirements of MRP
  LO 13.5 Describe some of the difficulties users have encountered with MRP
  LO 13.6 Describe MRP II and its benefits
  LO 13.7 Explain how an MRP system is useful in capacity requirements planning
  LO 13.8 Describe ERP, what it provides, and its hidden costs

## Slide 3: MRP
LO 13.2
Material requirements planning (MRP):
  A computer-based information system that translates master schedule requirements for end items into time-phased requirements for subassemblies, components, and raw materials
  The MRP is designed to answer three questions:
    What is needed?
    How much is needed?
    When is it needed?

## Slide 4: Overview of MRP
LO 13.2
Access the text alternative for slide images.

## Slide 5: MRP Inputs: Master Schedule
LO 13.2
Master schedule:
  One of three primary inputs in MRP; states which end items are to be produced, when these are needed, and in what quantities
  Managers like to plan far enough into the future so they have reasonable estimates of upcoming demands
  The master schedule should cover a period that is at least equivalent to the cumulative lead time
      Cumulative lead time
        The sum of the lead times that sequential phases of a process require, from ordering of parts or raw materials to completion of the final assembly

## Slide 6: Cumulative Lead Time
LO 13.2

## Slide 7: MRP Inputs: Bill of Materials
LO 13.2
Bill of Materials (BOM)
  A listing of all of the assemblies, subassemblies, parts, and raw materials needed to produce one unit of a product
  Product structure tree
    A visual depiction of the requirements in a bill of materials, where all components are listed by levels

## Slide 8: Assembly Diagram and Product Structure Tree
LO 13.2
Access the text alternative for slide images.

## Slide 9: Low-Level Coding
LO 13.2
Low-level coding
  Restructuring the bill of materials so that multiple occurrences of a component all coincide with the lowest level at which the component occurs
Access the text alternative for slide images.

## Slide 10: MRP Inputs: Inventory Records
LO 13.2
Inventory records
  Includes information on the status of each item by time period, called time buckets
    Information about
      Gross requirements
      Scheduled receipts
      Expected amount on hand
    Other details for each item such as
      Supplier
      Lead time
      Lot size policy
      Changes due to stock receipts and withdrawals
      Canceled orders and similar events

## Slide 11: Assembly Time Chart
LO 13.2

## Slide 12: MRP Outputs: Primary
LO 13.2
Primary Outputs
  Planned orders
    A schedule indicating the amount and timing of future orders
  Order releases
    Authorizing the execution of planned orders
  Changes
    Revisions of the dates or quantities, or the cancellation of orders

## Slide 13: MRP Outputs: Secondary
LO 13.2
Secondary Outputs
  Performance-control reports
    Evaluation of system operation, including deviations from plans and cost information
      for example missed deliveries and stockouts
  Planning reports
    Data useful for assessing future material requirements
      for example purchase commitments
  Exception reports
    Data on any major discrepancies encountered
      for example late and overdue orders, excessive scrap rates, requirements for nonexistent parts

## Slide 14: MRP Processing
LO 13.3
MRP processing takes the end item requirements specified by the master schedule and “explodes” them into time-phased requirements for assemblies, parts, and raw materials offset by lead times

## Slide 15: MRP Record
LO 13.3
Week Number | 1 | 2 | 3 | 4 | 5 | 6
Gross Requirements |  |  |  |  |  | 
Scheduled Receipts |  |  |  |  |  | 
Projected on hand |  |  |  |  |  | 
Net requirements |  |  |  |  |  | 
Planned-order receipt |  |  |  |  |  | 
Planned-order release |  |  |  |  |  | 
Gross requirements
  Total expected demand
Scheduled receipts
  Open orders scheduled to arrive
Projected Available
  Expected inventory on hand at the beginning of each time period

## Slide 16: MRP Record (cont.)
LO 13.3
Week Number | 1 | 2 | 3 | 4 | 5 | 6
Gross Requirements |  |  |  |  |  | 
Scheduled Receipts |  |  |  |  |  | 
Projected on hand |  |  |  |  |  | 
Net requirements |  |  |  |  |  | 
Planned-order receipt |  |  |  |  |  | 
Planned-order release |  |  |  |  |  | 
Net requirements
  Actual amount needed in each time period
Planned-order receipts
  Quantity expected to received at the beginning of the period offset by lead time
Planned-order releases
  Planned amount to order in each time period

## Slide 17: MRP: Development
LO 13.3
The MRP is based on the product structure tree diagram
Requirements are determined level by level, beginning with the end item and working down the tree
  The timing and quantity of each “parent” becomes the basis for determining the timing and quantity of the “children” items directly below it
  The “children” items then become the “parent” items for the next level, and so on

## Slide 18: Example MRP
LO 13.3

## Slide 19: Example MRP (cont.)
LO 13.3
Access the text alternative for slide images.

## Slide 20: Using the MRP
LO 13.3
Pegging
  The process of identifying the parent items that have generated a given set of material requirements for an item

## Slide 21: Updating the System
LO 13.3
An MRP is not a static document
  As time passes
    Some orders get completed
    Other orders are nearing completion
    New orders will have been entered
    Existing orders will have been altered
      Quantity changes
      Delays
      Missed deliveries

## Slide 22: Updating the System (cont.)
LO 13.3
Two basic systems
  Regenerative system
    Approach that updates MRP records periodically
      Essentially a batch system that compiles all changes that occur within the time interval and periodically updates the system
      A revised production plan is developed in the same way the original plan was developed
  Net-change system
    Approach that updates MRP records continuously
      The production plan is modified to reflect changes as they occur
      Only the changes are exploded through the system

## Slide 23: Other MRP Considerations: Safety Stock
LO 13.3
Safety Stock
  Theoretically, MRP systems should not require safety stock
  Variability may necessitate the strategic use of safety stock
    A bottleneck process or one with varying scrap rates may cause shortages in downstream operations
    Shortages may occur if orders are late or fabrication or assembly times are longer than expected
    When lead times are variable, the concept of safety time is often used
      Safety time
        Scheduling orders for arrival or completion sufficiently ahead of their need so that the probability of shortage is eliminated or significantly reduced

## Slide 24: Other MRP Considerations: Lot Sizing Rules
LO 13.3
Lot-for-Lot (L4L) ordering
  The order or run size is set equal to the demand for that period
  Minimizes investment in inventory
  Results in variable order quantities
  A new setup is required for each run
Economic Order Quantity (EOQ)
  Can lead to minimum costs if usage of item is fairly uniform
    This may be the case for some lower-level items that are common to different “parents”
    Less appropriate for ‘lumpy demand’ items because inventory remnants often result
Fixed Period Ordering
  Provides coverage for some predetermined number of periods

## Slide 25: MRP in Service
Material goods that form a part of product - service
  Food catering service
    Estimating quantities of ingredients
    Estimating delivery times

## Slide 26: MRP Benefits
LO 13.4
Enables managers to easily
  Determine the quantities of each component for a given order size
  Know when to release orders for each component
  Be alerted when items need attention
Additional benefits
  Low levels of in-process inventories
  The ability to track material requirements
  The ability to evaluate capacity requirements
  A means of allocating production time
  The ability to easily determine inventory usage via backflushing
      Exploding an end item’s BOM to determine the quantities of the components that were used to make the item

## Slide 27: MRP Requirements
LO 13.4
To implement an effective MRP system requires:
  A computer and the necessary software to handle computations and maintain records
  Accurate and up-to-date
    Master schedules
    Bills of materials
    Inventory records
  Integrity of data files

## Slide 28: MRP Difficulties
LO 13.5
Consequence of inaccurate data
  Missing parts
  Ordering incorrect numbers of items
  Inability to stay on schedule
Other problems
  Assumptions of constant lead times
  Products being produced differently from the BOM
  Failure to alter a BOM when customizing a product
  Inaccurate forecasts

## Slide 29: MRP II
LO 13.6
Manufacturing resources planning (MRP II)
  Expanded approach to production resource planning, involving other areas of the firm in the planning process and enabling capacity requirements planning
    Most MRP II systems have the capability of performing simulations to answer a variety of “what if” questions so they can gain a better appreciation of available options and their consequences

## Slide 30: MRP II: Overview
LO 13.6
Access the text alternative for slide images.

## Slide 31: Closed Loop MRP
LO 13.6
When MRP II systems began to include feedback loops, they were referred to as Closed Loop MRP
Closed Loop MRP
  Systems evaluate a proposed material plan relative to available capacity
  If a proposed plan is not feasible, it must be revised
    This evaluation is referred to as capacity requirements planning

## Slide 32: Capacity Requirements Planning
LO 13.7
Capacity requirements planning (CRP)
  The process of determining short-range capacity requirements.
  Inputs to capacity requirement planning
    Planned-order releases for the MRP
    Current shop loading
    Routing information
    Job time
  Key outputs
    Load reports for each work center

## Slide 33: Load Reports
LO 13.7
Load reports
  Department or work center reports that compare known and expected future capacity requirements with projected capacity availability

## Slide 34: Enterprise Resource Planning
LO 13.8
Enterprise resource planning (ERP)
  ERP was the next step in an evolution that began with MRP and evolved into MRPII
  ERP, like MRP II, typically has an MRP core
  ERP provides a system to capture and make data available in real time to decision makers and other users throughout an organization
  ERP systems are composed of a collection of integrated modules

## Slide 35: Overview of ERP Software Modules
LO 13.8
Module | Brief Description
Accounting/Finance | A central component of most ERP systems. It provides a range of financial reports, including general ledger, accounts payable, accounts receivable, payroll, income statements, and balance sheets
Marketing | Supports lead generation, target marketing, direct mail, and sales
Human Resources | Maintains a complete data base of employee information such as date of hire, salary, contact information, performance evaluations, and other pertinent information
Purchasing | Facilitates vendor selection, price negotiation, making purchasing decisions, and bill payment
Production Planning | Integrates information on forecasts, orders, production capacity, on-hand inventory quantities, bills of material, work in process, schedules, and production lead times
Inventory Management | Identifies inventory requirements, inventory availability, replenishment rules, and inventory tracking
Distribution | Contains information on third-party shippers, shipping and delivery schedules, delivery tracking
Sales | Information on orders, invoices, order tracking, and shipping
Supply Chain Management | Facilitates supplier and customer management, supply chain visibility, and event management

## Slide 36: ERP Project Organization
LO 13.8
The “big bang”
  Companies cast off all of their legacy systems at once and implement a single ERP system across the entire company
  The most ambitious and difficult implementation approach
Franchising strategy
  Independent ERP systems are installed in each business unit of the enterprise while linking common processes across the enterprise
  Suits large or diverse companies that do not share many common processes across business units
Slam dunk
  ERP dictates the process design where the focus is on a few key processes
  More appropriate for smaller companies expecting to grow into ERP

## Slide 37: ERP Considerations
LO 13.8
How can ERP improve a company’s business performance?
How long will an ERP implementation project take?
How will ERP affect current business processes?
What is the ERP total cost of ownership?
What are the hidden costs of ERP ownership?

## Slide 38: End of Main Content

## Slide 39: Accessibility Content: Text Alternatives for Images

## Slide 40: Overview of MRP - Text Alternative
Return to parent-slide containing images.
The inputs include the Master schedule (which includes orders and forecast), bill of materials (which includes design changes), inventory records (which includes receipts and withdrawals). These all lead to MRP computer programs, which leads to the following: primary reports (including planned-order schedules, order releases, and changes), secondary reports (including performance-control reports, planning reports, and exception reports, and inventory transactions (which is also included in inventory records).
Return to parent-slide containing images.

## Slide 41: Assembly Diagram and Product Structure Tree - Text Alternative
Return to parent-slide containing images.
The top of the drawing shows a finished chair, then a line splits into three sections for front legs and crossbar, seat, and back supports, crossbar, and side rails. The product structure tree starts with chair on top, then three segments to leg assembly, seat, and back assembly. The leg assembly includes the 2 legs and a crossbar. The back assembly includes 2 side rails, a crossbar, and 3 back supports.
Return to parent-slide containing images.

## Slide 42: Low-Level Coding - Text Alternative
Return to parent-slide containing images.
At the top is the finished product, X. below are two parts, B (with quantity 2) and C, then below B is D (quantity 3) and E, then below D is E (quantity 4); below C is E (quantity 2) and F (quantity 2).
Return to parent-slide containing images.

## Slide 43: Example MRP (cont.) - Text Alternative
Return to parent-slide containing images.
In Week 4, 100 shutters are needed; in Week 8, 150 are needed. These values are entered in the master schedule. In the first MRP, for shutters, 100 and 150 are entered in the columns for week 4 and 8 for gross requirements, for net requirements, and also for planned order receipts. These values are put in the columns for weeks 3 and 7, respectively, in the planned-order releases row. In the second MRP, for frames, 2 × 100 = 200 and 2 × 150 = 300 are entered under week 3 for gross requirements, net requirements, and planned-order receipts. The 200 and 300 are entered in week 1 for planned-order releases. In the third MRP, for wood sections, 4 × 100 = 400 and 4 × 150 = 600 are entered in week 3 for gross requirements. In the scheduled receipts row, 70 is entered for week 1. In the projected on hand row, 70 is entered for weeks 1, 2, and 3. In the net requirements and the planned-order receipts rows, 330 is entered in week 3 and 600 for week 7. For the planned-order releases, 330 is entered for week 2 and 600 for week 6.
Return to parent-slide containing images.

## Slide 44: MRP II: Overview - Text Alternative
Return to parent-slide containing images.
All flowing into Aggregate planning are Marketing, Finance, Market demand, and Manufacturing. From there is a question: Problems? Yes - adjust production plan. No - continue to Master production schedule, then to Capacity requirements planning. Question: Problems? Yes - go back to planning. No - proceed to MRP. Question - Problems? Yes - back to adjust MRP. No - Final material and requirement plans and capacity requirement plans.
Return to parent-slide containing images.